## Slide 1: Medical Data Manipulation and Preprocessing
SPARK March 29, 2025
Craig Jones, PhD

## Slide 2: Background
BSc (Hons) in Computing Science and Mathematics (Simon Fraser University)
MSc in Medical Biophysics (University of Western Ontario)
PhD in Physics (Medical Biophysics University of British Columbia)

## Slide 3: Background
25+ years in medical imaging (magnetic resonance imaging)

## Slide 4: Medical Image Processing
Regions of the Body
Images
File Formats
Processing Software
Signal, Noise, and Artifact
Signal Scaling
Segmentation
Registration / Alignment
Data Augmentation (PyTorch)

## Slide 5: Regions of the Body

## Slide 6: What regions of the body need to be imaged?

## Slide 7: Body Regions
Brain / head
Neck
Shoulder
Heart
Abdomen
Pelvis
Extremities

## Slide 8: Soft Tissue, Hard Tissue, Metabolism
Soft Tissue in the body (structure)
  Brain
  Muscle
  Tendons
Hard Tissue / Density (structure)
  Bone
  Tumor
  Blood
Metabolism (function)
  Glucose uptake
  Hyper-polarized
  Tumor uptake

## Slide 9: Images

## Slide 10: Interpretation of Numbers

## Slide 11: What is an image?
Images are made up of pixels (picture element) or voxels (volume element)
Numbers in images may represent a physical unit or a relative value
  CT images are in Hounsfield units (typically -500 – 3000)
  MRI images are relative signal units (typically 0 – 2500)
  absorption of high energy electromagnetic radiation from an x-ray tube in a patient
Human eye can distinguish approximately 100 shades of gray
Pixel

## Slide 12: Image Manipulation
All standard image manipulations can be done e.g., addition, subtraction etc.
X-Ray Image
2 * X-Ray Image
Random + X-Ray Image

## Slide 14: 2D vs 3D vs 4D
What is the difference between a 2D dataset and a 3D dataset?

## Slide 15: 2D vs 3D vs 4D
2D images are typically a single image
  May depend on acquisition type
3D images
  3 spatial directions, typically rows by columns by slices
4D
  3 spatial directions and a time direction
  Example is CT perfusion data or fMRI data

## Slide 16: Spatial vs Time Scans: CT Perfusion

## Slide 17: Pixel vs Voxel Dimension
In-plane pixel size is measured in millimeters
  CT is typically 0.5 mm x 0.5 mm
  MRI is typically 3 mm x 3 mm
All images have a thickness, typically in millimeters as well
Image thicknesses is typically larger than the in-place thickness
Some acquisitions might also have a “gap” between the images

## Slide 18: Image Field of View
Image field-of-view is the width and length of the image in real-world units (e.g., microns or millimeters)

## Slide 19: Gray Scale Images vs Color Images
Gray scale image is a single channel (rows by columns)
Color images are 3-channel
  Typically red, green, blue channels
  To make a gray scale image using 3-channels, copy the same value to all 3 channels

## Slide 20: Orientation of Images
Radiology convention is patient left on right side, patient right on left side of image
A
P
R
L
S
I
P
A
S
I
R
L

## Slide 21: Axial Sagittal Coronal
Axial
Sagittal
Coronal

## Slide 22: Medical Imaging File Formats

## Slide 23: Medical Imaging File Formats
What needs to be stored in a medical image?

## Slide 24: Various Imaging File Formats
JPEG / PNG / TIFF (not a medical imaging file format)
DICOM
NIFTI
MHA
MINC

## Slide 25: JPEG / PNG / TIFF
JPEG image files
  Most common file format available, digital photography
  Lossy or lossless compression
  Up to 10:1 compression
PNG
  Raster file format
  Supports lossless compression
  Transparency
… and Others
  GIF, BMP

## Slide 26: JPEG / PNG
Why are JPEG and PNG not good file formats to use for medical imaging?

## Slide 27: JPEG / PNG / TIFF
https://en.wikipedia.org/wiki/JPEG
No header
  Missing context about the image
  Missing scan information
  No voxel size or FOV information
Best to use other file formats for medical image processing.
Data is scaled to be 0 to 255
  … well, not necessarily for TIFF

## Slide 28: DICOM
Medical imaging standard (Medical Imaging & Technology Alliance)
Includes file format AND data exchange
“Part 5” alone is 154 pages of night time reading

## Slide 29: DICOM Image File Format
DICOM stores 1 image per file
  3D and 4D datasets are stored in a directory and can have 100s of files
Filenames are stored with a UID
Four levels of hierarchy
  Patient
    Information about the person
  Study
    Information about “today’s scan”
  Series
    A series is a single scan method (e.g., diffusion MRI scan)
  Instance
    The slice information
https://towardsdatascience.com/understanding-dicom-bce665e62b72

## Slide 30: DICOM Image File Format
A field in the header has three parts:
  Tag (a tuple of two values)
  Name
  Value
https://towardsdatascience.com/understanding-dicom-bce665e62b72

## Slide 31: DICOM Example

## Slide 32: DICOM Example
Data is stored in the attribute “pixel_array”
E.g.,
  dcm.pixel_array

## Slide 33: NIFTI (and Analyze)
Started out as “Analyze” file format
  .hdr and .img files separate
NIFTI format
  Header and data in one file (“.nii” or “.nii.gz”)
348 byte header
4+ dimensions of data can be stored (including pixel “size”)
Complete set of data types (8 bit to 128 bit)
Affine coordinate definitions relating voxel index to real world spatial index
https://nifti.nimh.nih.gov/nifti-1

## Slide 34: …And Others
MHA
  Associated with ITK
  Stores information when processed (e.g., registration or segmentation) through ITK
  Use “pip install medpy” to read MHA files in Python
MINC
  Medical Image NetCDF out of McGill
  “.mnc”
  https://www.mcgill.ca/bic/software/minc
AFNI
  “.brik” file format used primarily with AFNI software

## Slide 35: Python Software

## Slide 36: In Python…

## Slide 37: Saving NIFTI Data in Python
Three things needed when saving:
  Data
  Affine matrix
  Header
Affine matrix defines the mm to pixel scale and orientation
# Get the real, corrrect affine matrix from the PVP NIFTI filen = nib.load('filename_pvp_nifti_from_dicom.nii.gz’)
data = n.get_fdata()
# Save the data with the correct affine matrix as a NIFTI file.
new_nifti_data = nib.Nifti2Image(data,
affine=n.affine,
header=n.header)
new_nifit_data.save()

## Slide 38: Medical Image Processing Software

## Slide 39: MIPAV
MIPAV is a free visualization tool
https://mipav.cit.nih.gov

## Slide 40: ImageJ/FIJI
Free Java based visualization and quantitative processing software
https://imagej.net/software/fiji/

## Slide 41: MITK
Free visualization software based on ITK (Insight Toolkit)
https://www.mitk.org/wiki/The_Medical_Imaging_Interaction_Toolkit_(MITK)

## Slide 42: 3D Slicer
Free software for medical image visualization and processing
Python API to extend the features
https://www.slicer.org

## Slide 43: …and Others
BrainVoyager
  http://www.brainvoyager.com/
FSL
  https://fsl.fmrib.ox.ac.uk/fsl/fslwiki/
  Good image registration program
SPM
  https://www.fil.ion.ucl.ac.uk/spm/
AFNI
  https://afni.nimh.nih.gov

## Slide 44: Signal…

## Slide 45: What is Signal?

## Slide 46: Signal
Signal is the average pixel intensity in a region
where I(x,y) is the signal intensity at (x,y)
White matter mean signal is 763.6
… or …
(Not 763.6476475675677, why?)

## Slide 47: Noise vs Artifact
Noise
  contributions to a measured signal due to random processes
  contributions are of statistical nature and do not carry any information about the signal
Artifact
  part of the contents of an image that does not have a counterpart in the physical object being imaged; an artifact can appear as false structures
"Computed Tomography" by Willi A. Kalender, 2011

## Slide 48: Estimating Noise in an Image II
What contributes to the standard deviation of the signal in a region?
Noise in acquisition of the image
Artifacts in the image
Tissue heterogeneity

## Slide 49: Signal to Noise Ratio
Can we calculate an SNR in the tissue?
Well, it is difficult…

## Slide 50: Signal Scaling

## Slide 51: Signal Range
np.min(image) = -1024.0
np.max(image) = 1245.0
What is the range of signal in the image?

## Slide 52: Histogram

## Slide 53: Signal Scaled – Min/Max to 0/1

## Slide 54: Signal Normalization vs Standardization
dd_norm = (dd - np.min(dd)) / (np.max(dd) - np.min(dd))
dd_perc = np.clip((dd - np.percentile(dd, 0.1)) /
(np.percentile(dd, 99.9) - np.percentile(dd, 0.1)), 0, 1)
dd_std = (dd - np.mean(dd)) / np.std(dd)

## Slide 55: Signal Normalization vs Standardization
S_norm = (dd - np.min(S)) / (np.max(S) - np.min(S))
S_perc = np.clip((S - np.percentile(S, 0.1)) /
(np.percentile(S, 99.9) –
np.percentile(S, 0.1)), 0, 1)
S_std = (S - np.mean(S)) / np.std(S)

## Slide 56: Segmentation

## Slide 57: What is Segmentation?

## Slide 58: What is Segmentation?
the process of partitioning a digital image into multiple image segments, also known as image regions or image objects (sets of pixels)
https://en.wikipedia.org/wiki/Image_segmentation

## Slide 59: Segmentation Categories

## Slide 60: Segmentation Categories
Hard Segmentation
  Mask is binary (assuming two classes, background and lesion)
Fuzzy Segmentation
  Mask is floating point (typically range from 0 and 1)
  Each pixel is weighted by inclusion

## Slide 61: Segmentation Categories
Hard Segmentation
  Mask is binary (assuming two classes, background and lesion)
Fuzzy Segmentation
  Mask is floating point (typically range from 0 and 1)
  Each pixel is weighted by inclusion

## Slide 62: Hard Segmentation
Semantic segmentation: for every pixel, belonging class of the object

## Slide 63: Hard Segmentation
Instance segmentation: for every pixel, belonging class of the object
scipy.ndimage.label()

## Slide 64: Threshold Based Segmentation

## Slide 65: Threshold Based Segmentation
Histogram of the Image

## Slide 66: Histogram Threshold Values

## Slide 67: Threshold Segmentation Summary
Pros
  One of the simplest methods to segment an image
  Easy to choose a threshold value
  Segment into numerous regions
Cons
  Difficult to adapt to artifacts in the image
  All spatial information is lost
For most segmentation, neural networks and deep learning are likely going to be the direction to follow.

## Slide 68: Registration / Alignment

## Slide 69: What is registration or alignment?

## Slide 70: Types of Registration
Rigid Body
  Rotations and translations in 3D
  6 degrees of freedom
Affine Transformation
  Rotations, translations, scale, skew
  > 6 degrees of freedom
Deformable Registration
  Each voxel can move different amounts and directions
  Typically, for medical imaging, |J| < 0 (no “ripping” of the image)

## Slide 71: Algorithms for Medical Image Registration
Flirt
  Very old, stable code for aligning medical images
  https://fsl.fmrib.ox.ac.uk/fsl/fslwiki/FLIRT
  Simple call structure, very slow
ANTS Syn
  Advanced normalization tools
  https://github.com/ANTsX/ANTs
  Very complex call structure but fast.
IITK
  https://examples.itk.org/src/registration/

## Slide 72: ANTS
$ antsRegistrationSyn.sh -d 3 -f $template -m $moving -o output_rigid -t r -p f
Results in:
antsRegistration --verbose 1 --dimensionality 3 --float 1 --collapse-output-transforms 1 --output [ output_rigid,output_rigidWarped.nii.gz,output_rigidInverseWarped.nii.gz ] --interpolation Linear --use-histogram-matching 0 --winsorize-image-intensities [ 0.005,0.995 ] --initial-moving-transform [ tt_BR_T2W_FLAIRSENSE_20091124103934_6.nii.gz,tt_WIPBR_T2W_FLAIRSENSE_20140529105838_6.nii.gz,1 ] --transform Rigid[ 0.1 ] --metric MI[ tt_BR_T2W_FLAIRSENSE_20091124103934_6.nii.gz,tt_WIPBR_T2W_FLAIRSENSE_20140529105838_6.nii.gz,1,32,Regular,0.25 ] --convergence [ 1000x500x250x100,1e-6,10 ] --shrink-factors 8x4x2x1 --smoothing-sigmas 3x2x1x0vox
Template/Static
Moving
Aligned
2009 Scan
2014 Scan
2014 Aligned to 2009

## Slide 73: Data and Neural Networks
What is Data Augmentation?

## Slide 74: Data and Neural Networks
Load the Training and Validation Data
Setup Data Augmentation
Setup model, loss function and optimizer
Load Batch of Training Data
Epoch Loop
Training
Evaluate the Model
Compute Training Loss
Run Back Propagation
Compute Training Metrics
Load Batch of Validation Data
Validation
Evaluate the Model
Compute the Validation Loss
Compute Validation Metrics
Data
Augmentation

## Slide 75: Data and Neural Networks – Pre-Processing

## Slide 76: Data and Neural Networks - Augmentation

## Slide 77: Python Software Packages to Use
scipy.ndimage
SciKit Learn
SciKit Image
Numpy
TorchIO
Albumentations
Jupyter Notebooks

## Slide 78: Data Sources
https://medmnist.com
https://www.kaggle.com/datasets/andrewmvd/medical-mnist
https://www.kaggle.com/datasets

## Slide 79: PyTorch Dataset and DataLoaders

## Slide 80: PyTorch Dataset and DataLoader
PyTorch Dataset
Can be in memory or on disk
0
1
2
3
4
5 ….
3

## Slide 81: PyTorch Dataset and DataLoader
PyTorch Dataset
PyTorch DataLoader
Can be in memory or on disk
0
1
2
3
4
5 ….
0
1
2
3
Batch processing

## Slide 82: PyTorch Dataset and DataLoader
PyTorch Dataset
PyTorch DataLoader
Can be in memory or on disk
0
1
2
3
4
5 ….
0
1
2
3
Batch processing
Transform Applied

## Slide 83: PyTorch Dataset and DataLoader
Transforms, defined in TorchIO or Monai
Large number of pre-processing and augmentation

## Slide 84: PyTorch Dataset and DataLoader
Transforms, defined in TorchIO or Monai
Large number of pre-processing and augmentation
Why are these different??

## Slide 85: Pre-Processing Options
Intensity
  RescaleIntensity
    RescaleIntensity
  ZNormalization
    ZNormalization
  HistogramStandardization
    HistogramStandardization
      HistogramStandardization.train()
  Mask
    Mask
  Clamp
    Clamp
  NormalizationTransform
    NormalizationTransform
Spatial
  CropOrPad
    CropOrPad
      CropOrPad._get_six_bounds_parameters()
  ToCanonical
    ToCanonical
  Resample
    Resample
  Resize
    Resize
  EnsureShapeMultiple
    EnsureShapeMultiple
  CopyAffine
    CopyAffine
  Crop
    Crop
  Pad
    Pad

## Slide 86: Data Augmentation Options
Composition
  Compose
    Compose
  OneOf
    OneOf
Spatial
  RandomFlip
    RandomFlip
  RandomAffine
    RandomAffine
  RandomElasticDeformation
    RandomElasticDeformation
  RandomAnisotropy
    RandomAnisotropy
Intensity
  RandomMotion
    RandomMotion
  RandomGhosting
    RandomGhosting
  RandomSpike
    RandomSpike
  RandomBiasField
    RandomBiasField
  RandomBlur
    RandomBlur
  RandomNoise
    RandomNoise
  RandomSwap
    RandomSwap
  RandomLabelsToImage
    RandomLabelsToImage
  RandomGamma
    RandomGamma

## Slide 87: Data Augmentation – What do I use??
Pre-processing
  First, look at the model and see if there are pre-processing requirements
  e.g, signal scaled from 0-1
  Then, see if re-normalizing the histogram would be helpful
Data Augmentation (increase dataset size or in-training augmentation)
  Always want to use for in-training augmentation
  Generally, choose transforms that change the data, a little
  Will the augmented data look like test data (non-augmented)

## Slide 88: PyTorch Dataset and DataLoader
Dataset represents the set of data
Must have a method to get one data (__getitem__)
The “transform” is the data augmentation transform.

## Slide 89: PyTorch Dataset and DataLoader
DataLoader takes:
  Dataset
  Batch size
During training , Load from batch
Load the Training and Validation Data
Setup Data Augmentation
Setup model, loss function and optimizer
Load Batch of Training Data
Epoch Loop
Training
Evaluate the Model
Compute Training Loss
Run Back Propagation
Compute Training Metrics
Load Batch of Validation Data
Validation
Evaluate the Model
Compute the Validation Loss
Compute Validation Metrics

## Slide 90: Medical Data Manipulation and Preprocessing
Questions?
Regions of the Body
Images
File Formats
Processing Software
Signal, Noise, and Artifact
Signal Scaling
Segmentation
Registration / Alignment
Data Augmentation (PyTorch)